## Slide 1: Overscan and sync scrolling
“it’s cycles all the way down”
by Troed of SYNC

## Slide 2
Overscan
Sync lock
Sync scrolling

## Slide 3: Credits
Paulo Simoes (LJBK)
Ijor
Alien / ST Connexion
.. and a little bit me

## Slide 4: Overscan

## Slide 5: History
[lower] Border removal invented by Alyssa, released by TEX Sept 1987
[right] First released by TEX (Amiga demo, March 1988)
[left] First released by TNT Crew (Death of the Left Border, 1988)

## Slide 6
[upper (60Hz)] First released by XXX International (July 1988)
[upper (50Hz)] First released by TCB (Swedish New Years 88-89)
[fullscreen (unstable)] First released by Omega (Omega Demo, Dec -88)
[fullscreen (stable)] First released by Level 16 (Union Demo, Jan -89)

## Slide 7: Stabilizer
A Shifter necessity

## Slide 8: Two commonly used variants
444: HI nop LO (Ilja, Level 16)
440: MED nop nop LO (Gunstick, ULM)
One cancels HBLANK, one shows pixel data

## Slide 9: Forget all you know about switches
move.b d1,(a2) * left
nop
move.b d0,(a2)
89 nop
move.b d0,(a1) * right
move.b d1,(a1)
13 nop
move.b d1,(a2) * stabiliser
nop
move.b d0,(a2)
12 nop

## Slide 10
GLUE statemachine
(ST)
Notes: See http://www.atari-wiki.com/?title=ST_STE_Scanlines for the full writeup

## Slide 11: Wakestates
2006 “cold & warm wakeup modes”
2012 “WS1-4” – 2 cycle precision
Research mostly by Paulo Simoes (LJBK)
Before this everyone thought it was due to multiple revisions of Atari hw

## Slide 12: GLUE-CPU unsync
Offset 0 reads values at cycle 56 (FREQ) and 57 (RES)
Offset 1 reads values at cycle 57 (FREQ) and 58 (RES)
Offset 2 reads values at cycle 58 (FREQ) and 59 (RES)
Offset 3 reads values at cycle 59 (FREQ) and 60 (RES)

## Slide 13: GLUE-CPU unsync
WS1 (DL6): Changes made by 56 (FREQ), 56 (RES)
WS3 (DL5): Changes made by 56 (FREQ), 58 (RES)
WS4 (DL4): Changes made by 58 (FREQ), 58 (RES)
WS2 (DL3): Changes made by 58 (FREQ), 60 (RES)
… we do have 2 cycle granularity!

## Slide 14: Classic demos with WS effects
TCB snow screen in Swedish New Years 89-90
  Someone might well have gotten the idea for sync scrolling from that effect
ULM fullscreen issue

## Slide 15: 230 and 224 byte fullscreen lines
Leonard / Oxygene stumbled upon “short left border” in 2006 (atari-forum thread)
  Re-discovered and now popularized by DHS

## Slide 16
GLUE statemachine
(STE)
Notes: See http://www.atari-wiki.com/?title=ST_STE_Scanlines for the full writeup

## Slide 18: Optimized fullscreen line
0: HI
8: 50Hz
16: LO
376: 60Hz

## Slide 19: Stabilize somewhere else?
0: HI
8: MED
16: LO
24: 50Hz
376: 60Hz
472 cycles free compared to 456
– separated into two vs three blocks

## Slide 20: Current status
ST WS1, WS3, WS4
ST WS2 – but depending on Shifter state
STE – maybe (noticed yesterday!)

## Slide 21
415
X
276*

## Slide 23: Sync lock

## Slide 24: Regular sync lock
Read video pointer, invert delay, done
Top image line needed for sync

## Slide 25: HBL sync lock
Ijor (thread on Atari-Forum)
68000 auto vector E-clock
  Detect the jitter
  Insert anti-pattern at HBL line 33
Adds an extra fullscreen line, allows all combinations on first line
Notes: http://www.atari-forum.com/viewtopic.php?f=68&t=9527&hilit=68000+clock+cycles+table&start=125

## Slide 27: Sync scrolling

## Slide 28: Sync scrolling
TCB (Cuddly/SoWatt/Enchanted Lands)
  Only left/right borders – 15 lines
Sync (Swedish New Year 89-90)
  9 lines
Griff / Inner Circle
  7 lines
…

## Slide 29
12 line length combos
=
All 128 offsets in just 4 lines
Notes: See http://www.atari-wiki.com/?title=ST_STE_Scanlines for how these values are calculated

## Slide 30: GLUE is not alone in this
4 pixel fullscreen sync scrolling (Alien)
4 pixel non-fullscreen sync scrolling (LJBK)
These are Shifter effects

## Slide 32: Shifter statemachine
Number_of_read_bitplanes = 0
REPEAT
IF Load is active THEN IR[Number_of_read_bitplanes] = Data sent from MMU
Number_of_read_bitplanes = Number_of_read_bitplanes + 1
IF Number_of_read_bitplanes == 4 AND IF DE is active
THEN RR1 = IR1; RR2 = IR2; RR3 = IR3; RR4 = IR4
IF Number_of_read_bitplanes == 4 THEN Number_of_read_bitplanes = 0
END_REPEAT

## Slide 33: 4 pixel sync scroll
Alien/ST Connexion in Punish Your Machine
Open left border (HI)
Go to medium res
Wait X cycles
Go to low res

## Slide 34: “Oh crap shifted bitplanes”
All coders ever have written a fullscreen has seen this
… exploited by LJBK (Paulo Simoes) in 2012

## Slide 35: LJBK’s 4 pixel non-fullscreen sync scroll
Deterministically unstabilize
the Shifter leaving a predictable number of words before screen start …
… and get it to work in all wakestates …
… and …
Notes: http://www.atari-forum.com/viewtopic.php?f=16&t=24855&hilit=horisontal&start=275

## Slide 36: Current status
0, -4, -8, -12 in WS2, WS4 & often WS3
0, -4, -8 in WS3 (sometimes) and WS1
Viewer has to select which method is non-banded. Wait, what’s “banded”?

## Slide 37: Only 4 wakestates?
Banded lines
Spectrum 512 pixels
Possible internal Shifter clocks, or MMU desync
Migratory states

## Slide 40: “Every 16 pixels”
The most important substate to solve for future ST/STE overscan insights
Now comes tentative research …

## Slide 42
Seems to depend on memory address, so, entering C64 VSP territory …
“The dreaded VSP crash is caused by a metastability condition in the DRAM.”
http://www.linusakesson.net/scene/safevsp/

## Slide 43: What’s next?
Snooping the data bus :P

## Slide 44: LET’S WRAP